## Slide 1: CISCO ROUTING PROTOCOL
Present by :
Engg. Kazi Mohammad Ahsanul Haque
CCNA, RHCSA, RHCE, MCP, RHCVA
Mobile: 01742618969
Email: ahsan296@gmail.com

## Slide 2: What is routing protocol ?
A routing protocol is a set of rules used by routers to determine the most appropriate paths into which they should forward packets towards their intended destinations.
A routing protocol specifies how routers communicate with each other.

## Slide 3
Routing protocol are 2 types : ( Base on routing table )
1.Static routing
2. Dynamic routing
TYPE OF ROUTING PROTOCOL ?

## Slide 4
What is static routing ?
Static routing is a form of routing that occurs when a router uses a manually-configured routing entry.
Static routing is a method of routing where every configuration (example: network path , next network addresse, etc. ) is configured by network administrator.

## Slide 5
Benefit of static routing:
This provides a granular level of control over routing.
Routers will not share static routes with each other.
Static routing reducing CPU/RAM overhead and saving bandwidth.
Static routes have an Administrative Distance (AD) of 1, and thus are always preferred over dynamic routes.

## Slide 6
Demerits of Static routing :
Static routing is not fault-tolerant.
Any change to the routing infrastructure (such as a link going down, or a new network added) requires manual intervention .
Cannot seamlessly choose a better route if a link becomes unavailable.

## Slide 7
What is Dynamic routing ?
A dynamic routing table is created, maintained, and updated by a routing protocol running on the router.
Dynamic routing enables routers to select paths according to real-time logical network layout changes. RIP, EIGRP,OSPF etc are some dynamic routing protocol

## Slide 8
Benefit of dynamic routing:
Routers do share dynamic routing information with each other .
routing protocols are capable of dynamically choosing a different (or better) path when there is a change to the routing infrastructure.
No manual inter vation required.
No need to calculate routing path .
Simpler to configure on larger networks .
Ability to load balance between multiple links .
Updates are shared between routers, thus consuming bandwidth.

## Slide 9
Demerits of dynamic routing :